## Slide 1: The Background of Nominal Unit shear strength(Vs) for shear wall in US standard
Li Rui ＆ Zhao Jianchi
Notes: Today’s topic is the question that isoda sensei gives us, So I use this as the topic.

## Slide 2: Content
Introduction
Specimen
Test setup
Test Procedure
Calculation
Reference
Notes: I will introduce follow this content, and during my introduce I will make comparison between Japanese Standard with US standard

## Slide 3: Introduction
Vs : Tabulated Nominal Unit Shear strength
Use in Allowable Stress Design method(ASD) and Load Resistance Factor Design method(LRFD)
1 plf(pound per linear foot)→14.59 N/m
Determine allowable unit shear strength
Notes: First what is Vs, Vs is a nominal unit shear strength tabulated in SDPWS building standard, it can be used to calculate the allowable unit shear strength by multiplying or dividing some factors. And this allowable unit shear strength will be used in ASD and LRFD design method. The unit of the Vs is pound per linear foot, and can be transferred to KN/m

## Slide 4: Introduction
ASTM E2126- Cyclic Load Test for Shear Resistance of Vertical Element of the lateral Force Resisting System for Buildings
ASTM-American Society for Testing and Materials
ASTM E564- Static Load Test for Shear Resistance of Framed Walls for Building(basic test for ASTM 2126)
Vs
First Major Event (FME)
Ultimate displacement (Δm)
Notes: Vs was tested according to ASTMxxxxxxx, u can see the title of the standard, and the mainly difference is one is xxx the static load. And Static load is used to determine the FEM and Δm. Talking about FEM. Today we mainly focus on the Vs determine method, so we mainly focus on ASTM E2126

## Slide 5: Introduction
First Major Event (FME)
The FEM is the first significant limit state that occurs during the test.
The limit state is an event demarks the two behavior states, at which time some structural behavior of the specimen is altered significantly.
FME is determine by conducting monotonic load test.
Example:
Typical 8-ft(2.4-mm) wall
wood-framed walls with wood structural panel sheathing-Aspect ratio (h/b) of 2:1 or less. FME=0.8 in.(20mm); aspect ratio of 4:1, FME= 1.2 in(31mm)
Wood-framed walls with gypsum sheathing-Aspect ratio of 2:1 or less, FME=0.25 in(6.4mm)
Notes: Vs was tested according to ASTMxxxxxxx, u can see the title of the standard, and the mainly difference is one is xxx the static load. And Static load is used to determine the FEM and Δm. Talking about FEM. Today we mainly focus on the Vs determine method, so we mainly focus on ASTM E2126

## Slide 6: Specimens-ASTM E2126
Tested Shear wall
Frame
Bracing element
Sheathing Panel Attachments
Attachment to the Test base
Panel sheathing
Diagonal bracing
fastening
Connection
Type
Spacing edge distance of fasteners
Spacing of the shear connections and hold-down connectors
Notes: First lets talking about the specimens, as u might know the wood-framed shear wall is influenced by a lot of factors like frame, bracing element…..xxxxx, so each individual wall has its own value of Vs. before we conduct our test we should determine which kind of shear wall we are purposed on. All the material and test setup should representive of those to be used in the actual building construction.

## Slide 7: Test setup
Hold-down
Anchors
Optional horiz. joint
(枠組壁工法耐力壁及びその倍率性能試験・評価業務方法書 日本建築総合試験所）
（ASTM E2126)

## Slide 8: Test setup
If necessary both Japan and US use the tie-rod method

## Slide 9: Test procedure-loading method
Consists of two pattern.
The first pattern consists of three phase, at displacements representing 25%, 50%, 75% of anticipated FME.
Method-A SPD method
(Sequential-phased Displacement Procedure)
Notes: The cyclic displacement of the actuator shall be controlled to follow three kinds of loading method.
The second pattern is also increase 25% of each phase， lets enlarge one phase

## Slide 10: Test procedure-loading method
Each phase of the second pattern contains one initial cycle, three decay cycles, and a number of stabilization cycles. For nailed wood frame walls, three stabilization cycles is enough.
The amplitude of each decay cycle decreases by 25% of initial displacement.
Method-A SPD method
(Sequential-phased Displacement Procedure)

## Slide 11: Test procedure-loading method
ISO Displacement Schedule includes 2 patterns
The first displacement pattern consists of five single fully reversed cycles at displacements of 1.25 %, 2.5 %, 5 %, 7.5 %, and 10 % of the ultimate displacement ∆ m .
The second displacement pattern consists of phases, each containing three fully reversed cycles of equal amplitude, at displacements of 20 %, 40 %, 60 %, 80 %,100 %, and 120 % of the ultimate displacement ∆m
Method-B ISO method

## Slide 12: Test procedure-loading method
CUREE involves displacement cycles grouped in phases at increasing displacement levels.
Starts with a series of initiation cycles at small, equal amplitudes.
Then, each phase of the loading consists of a primary cycle with amplitude expressed as a fraction of the reference deformation and subsequent trailing cycles with amplitude of 75% of the primary one.
Method-C CUREE method

## Slide 13
Method A vs Method B
Method A maybe applicable when Fme is the yield limit state or for testing slack systems to determine a lower bound displacement causing hysteretic energy dissipation
Method B may be more applicable to systems that exhibit linear elastic behavior where FME is the strength limit state. If the ratio of Δm and FME is less than three, Method B may be preferable
Test procedure-loading method
Method C
The latest method。
For me now is a mystery

## Slide 14: Test procedure-loading method
There are two loading methods in Japanese standard.
First one is used in tie-rot type.
Each phase of that procedure consists of three fully reversed cycles, associating with a respective displacement level of 1/600, 1/450, 1/300, 1/200, 1/150, 1/100, 1/75, 1/50rad.
When it comes to the maximum load stress , continue loading until deformation angle comes to 1/15 or load stress decrease to 80% of the max load stress.
The second method is for no tie-rot type.
Each phase of this method also consists of three fully reversed cycles, and associates with a respective displacement level of 1/450, 1/300, 1/200, 1/150, 1/100, 1/75, 1/50rad.
When it comes to the maximum load stress , continue loading until deformation angle comes to 1/15 or load stress decrease to 80% of the max load stress.

## Slide 15: Calculation
Failure limit state----Δu(in cyclic test), Δm (in monotonic test)
Strength limit state----Δpeak，PPeak
Yield limit state----Δyield, Pyield
Notes: Envelop curve is determined using load-displacement data from the test, Py

## Slide 16: Calculation
Shear strength(Vpeak)
Ppeak= maximum load resisted by the specimen in the given envelope, lbf(N); and
L = length of specimen, ft(m)
unite ----- lbf/ft or N/m
Allowable strength Pa
Pa
Py
0.2Pu(
2/3Pmax
P1/120 or P2/150
Pmax= maximum load resisted by the specimen in the given envelope; N; and
Pu=Ultimate strength, N ; and
u = yield ratio calculated Du divided Dy multiplied by Pu/Py
Vpeak is the tabulated design value in US standard
倍率 is the tabulated unit design value in Japanese standard
Notes: 0.8pmax or displacement corresponding to 1/15

## Slide 17: Reference
ASTM E2126-11 Standard Test Method for Cyclic (Reversed) Load Test for Shear Resistance of Vertical Elements of the Lateral Force Resisting Systems of Buildings
木造軸組工法住宅の許容応力度設計（２００８年版）
枠組壁工法耐力壁及びその倍率性能試験・評価業務方法書